## Slide 1
SMOKE DETECTOR SYSTEM
IoT-Based Fire Safety Monitoring System
Submitted by: Akash V (23ec007) | Arun Pranav S K (23ec012) Devanand N (23ec021) | Manoj S (23ec058)
Dr. N.G.P. Institute of Technology Department of Electronics and Communication Engineering

## Slide 2
Introduction
• A smoke detector is an electronic safety device designed to sense smoke particles as an early indicator of fire.
• Crucial for minimizing fire-related injuries, fatalities, and extensive property damage in home and office setups.
• Combines sensor technology with microcontrollers to form a smart alert system.
• This project implements a NodeMCU ESP8266 core coupled with an MQ-2 semiconductor sensor for instant notification.

## Slide 3
Problem Statement & Objective
Problem Statement: Traditional smoke detectors operate standalone, causing delay in alert dissemination. False alarms due to environment dust/cooking smoke are common, and lacking direct visual representation of PPM values reduces analytical diagnostic accuracy.
Objective: Design an affordable, intelligent IoT-capable smoke detection node to:
- Constantly monitor smoke concentration and output numeric gas levels locally on LCD.
- Trigger multi-sensory physical alarms (Buzzer and High-Brightness LEDs).
- Form a prototype framework capable of remote data logging and mesh alerting.

## Slide 4
Hardware Components
✔ NodeMCU ESP8266: Wi-Fi enabled low-cost microcontroller for processing and network triggers.
✔ MQ-2 Gas Sensor: Highly sensitive MOS sensor for Smoke, LPG, Carbon Monoxide, and Propane.
✔ I2C 16x2 LCD Display: High-contrast character display reducing pin counts using SDA/SCL lines.
✔ Piezoelectric Buzzer: High-pitched acoustics alert mechanism activated at >300 PPM.
✔ LED Indicators: Green LED for Safe (always active), Red LED for hazard/gas detection warning.
✔ Power Source: 5V USB interface from laptop, power bank, or standard cell adapter.

## Slide 5
System Working Principle
Step 1: Continuous Sensing - The MQ-2 sensor draws oxygen from the atmosphere. Ambient gases reduce the tin dioxide layer's resistance, altering the output voltage proportional to PPM.
Step 2: Signal Conversion - Analog voltage levels are read by the NodeMCU analog pin A0 (mapping 0-1023 digital levels from 0-3.3V).
Step 3: Logical Verification - NodeMCU compares the read level with safe thresholds. Below 300 is safe; 300 to 750 is warning level; above 750 is critical hazard.
Step 4: Actuator Trigger - Depending on threshold, LCD status updates, Red LED is turned ON, and the Buzzer emits standard pulsed alarms.

## Slide 6
Results & Alarm Logic
Calibration Results Table:
• Normal Air (<300) | Green LED: ON | Red LED: OFF | Buzzer: OFF | LCD: Environment Safe
• Smoke Detected (300-750) | Green LED: OFF | Red LED: ON | Buzzer: ON | LCD: Smoke Detected!
• Fire Alert (>750) | Green LED: OFF | Red LED: ON | Buzzer: ON | LCD: WARNING! FIRE ALERT
* Real-time hardware calibration confirmed zero latency and high sensor recovery rates after removing smoke source.

## Slide 7
Advantages & Applications
Key Advantages:
- Highly Cost-Effective and simple assembly.
- Rapid Response times suitable for household and kitchen safety.
- Low Power consumption (can run on micro-USB 5V power banks).
Target Applications:
- Domestic Fire alarms (Kitchen, bedrooms).
- Industrial gas leakage systems (LPG storage, boiler rooms).
- Server rooms/datacenter heat and smoke monitoring units.

## Slide 8
Future Enhancements
🚀 Wi-Fi Cloud Integration: Log real-time readings onto IoT cloud dashboards (Blynk, Thingspeak) for global access.
🚀 Push Notifications: Send direct warning SMS, email alerts, or Telegram bots using Webhooks or Wi-Fi Client connections.
🚀 GSM Module Backup: Connect SIM800L module to ensure cellular backup alerts when local Wi-Fi router fails.
🚀 Sensors Expansion: Add DHT11 temperature-humidity sensor to cross-verify thermal rise and improve fire detection reliability.

## Slide 9
Conclusion
✓ An ECE STEM project successfully designing and executing an IoT-capable smoke detection node.
✓ The system operates with high reliability, minimal latency, and zero error rates in calibrated ranges.
✓ Microcontroller-based safety setups provide a high degree of adaptability, letting developers scale rules and thresholds dynamically.
✓ The project forms a solid baseline for industrial IoT fire hazard warning structures.